Division 1				  General Requirements

Prohibition of Asbestos Containing Materials

Section 01900

THIS SECTION MUST BE EDITED BY PROJECT MANAGER TO MEET SPECIFIC PROJECT NEEDS.

ARTICLE 1 - GENERAL

1.1  RELATED DOCUMENTS

The following documents are a part of this section:

All documents in Bidding Requirements, Contract Forms and Conditions of the Contract.

Other sections of Division 1 - General Requirements apply to this section.

1.2  DESCRIPTION AND INTENT OF THE WORK

No asbestos containing material (ACM) shall be brought onto the Project site, and/or incorporated into the Project construction without the written consent of the Owner.  Any asbestos containing material found at any time including after contract completion, to have been brought onto the site or incorporated into the Project construction by the Contractor, or any Subcontractors, Sub-Subcontractors or Suppliers, shall be removed and disposed of in accordance with the then current governmental regulatory standards.

All costs associated with the inspection, sampling, testing, removal and disposal of ACM as described above shall be paid by the Contractor.

1.3  DEFINITIONS

ASBESTOS:  The asbestiform varieties of serpentine (chrysotile), riebeckite (crocidolite) cummingtonite-grunerite (amosite), anthophyllite, actinolite and tremolite.

ASBESTOS CONTAINING MATERIAL (ACM):  Any material containing more than one percent (1%) by weight of asbestos of any type or mixture of types.

ASBESTOS CONTAINING BUILDING MATERIAL (ACBM):  Any material used in the construction of, or incorporated into the construction of, any building that contains more than one percent (1%) by weight of asbestos of any type or mixture of types.

MSDS: A material safety data sheet (MSDS) is a form containing data regarding the properties of component   substances that comprise a manufactured product. They are a basic hazard communication tool that gives details on chemical and physical dangers, safety procedures, and emergency responses for chemicals.

1.4  QUALITY ASSURANCE

Project Manager shall insert  E/A Statements into the manual or edit Article 1.4.

PROHIBITION OF ASBESTOS CONTAINING MATERIALS

The E/A has been instructed to not permit any asbestos containing materials to be specified, requested or approved for use in conjunction with this Project.

If authorized by the Asbestos and Lead Management Group of Public Works, the Project Manager may delete the following paragraphs, down to “Asbestos Containing Materials Prohibited from Site”.

The E/A has signed the following:

A. 01900A Statement of Non-Inclusion of Asbestos Containing Material (E/A, Prior to Design):  stating that the Engineer/Architect shall not specify, request or approve any ACM in this Project without prior written approval of Owner.

B.  01900B Statement of Non-Inclusion of Asbestos Containing Material (E/A, After Design):  stating that the Engineer/Architect has not specified, requested or approved any ACM in this Project without the prior written approval of the Owner, and that any ACM allowed in this Project is identified in the Statements.

These Statements are included in the Construction Documents.

ASBESTOS CONTAINING MATERIALS PROHIBITED FROM SITE

No asbestos containing materials will be permitted as part of the Project construction.  The following list is intended to be used as a general guide to show which types of materials are suspected to contain asbestos:

| Cement Pipes | Elevator Brake Shoes |
| --- | --- |
| Cement Wallboard | HVAC Duct Insulation |
| Cement Siding | Boiler Insulation |
| Asphalt Floor Tile | Breeching Insulation |
| Vinyl Floor Tile | Ductwork Flexible Fabric Connections |
| Vinyl Sheet Flooring/vinyl wall coverings | Cooling Towers |
| Flooring Backing | Pipe Insulation (corrugated air-cell, block, etc.) |
| Construction Mastics (floor tile, carpet, ceiling tile, etc.) | Heating and Electrical Ducts |
| Acoustical Plaster | Electrical Panel Partitions |
| Decorative Plaster / stucco | Electric Cloth |
| Textured Paintings/Coatings | Electric Wiring Insulation |
| Ceiling Tiles and Lay-in Panels | Chalkboards |
| Spray-Applied Insulation | Roofing Shingles / tiles / membranes |
| Blown-in Insulation | Roofing Felt |
| Fireproofing Materials | Roof Coatings |
| Taping Compounds (thermal) | Base Flashing |
| Packing Materials (for wall/floor penetrations) | Thermal Paper Products |
| High Temperature Gaskets | Fire Doors |
| Laboratory Gloves | Caulking/Putties |
| Fire Blankets | Adhesives / mastics |
| Fire Curtains | Wallboard |
| Elevator Equipment Panels | Joint Compounds |
|  | Spackling Compounds |
|  | Laboratory hoods/tabletops |
|  | CMU block fill materials |

If any of these suspect materials are specified for use on the Project, and if they do not have specific labelling identifying them as asbestos free, then the CONTRACTOR shall notify the OWNER immediately.  Laboratory analysis of the material by an OWNER-approved laboratory shall be performed at CONTRACTOR's expense in order to warrant that the material does not contain asbestos.  A copy of the package labelling or results of laboratory testing must be provided to the OWNER prior to inclusion of the specified material during construction. Contractor’s construction submittals must include MSDSs for all new materials used in construction of buildings, facilties and infrastructure.

1.5  SUBMITTALS

NON-USE OF ASBESTOS AFFIDAVITS

At the time that the Contractor signs the Agreement, they shall sign a Non-Use of Asbestos Affidavit (Contractor Prior to Construction), Contract Document 00680. This Affidavit certifies that the Contractor agrees that they will not allow any asbestos containing materials to be incorporated into the construction of the Project or allow any asbestos containing building materials on the site for which the Owner has not given prior written approval.

Prior to final payment, the Contractor will provide to the OWNER a Non-Use of Asbestos Affidavit (Contractor After Construction), Contract Document 00681. This Affidavit certifies that the Contractor did not allow asbestos containing materials to be incorporated into the construction or allowed any asbestos containing building materials on the site for which the Owner of the Project did not give prior written approval.

ASBESTOS CONTAINING MATERIALS:  When any asbestos containing materials are used on the Project, provide the following information:

A detailed description of the material containing the asbestos.

The type and percent of asbestos contained in the material.

The quantity of the materials used, including the square footage, or in the case of pipe insulation, the size and linear footage.

A drawing showing the exact location of any asbestos containing materials.

Final payment shall be withheld until the above described Affidavits, submittals and/or information are received and approved.

Project Manager shall insert  E/A Statements into the manual or edit Article 1.4.

END